ORDER DESCRIPTION

- Object of the contract

The subject of the order is the supply of fiber optic patch cables, listed below by name and quantity needed:

- Fiber Optic Patch Cables MIR type I		2 pcs.

- Fiber Optic Patch Cables MIR type II		4 pcs.

- Fiber Optic Patch Cables MIR type III		4 pcs.

- Parameters

  - PART I Fiber Optic Patch Cables MIR type I

| Product name | Parameter | Specification |
| --- | --- | --- |
| Fiber Optic Patch Cables MIR type I | Quantity | 2 szt. |
|  | Fiber | InF2 |
|  | Diameter Core | 9 um +/- 0.5 um |
|  | Numerical aperture | 0.26 +/- 10% in terms of 3.5-5.5 um |
|  | Attenuation | - no more than 0.5 dB/m in terms of 3-4.5 um - no more than 3 dB/m in terms of 4.5-5.5 um |
|  | Length patchord | 1 m +/- 10% |
|  | Diameter outer of the patchcord sheath | 3 mm +/- 10% lub 2 mm +/- 10 % |
|  | Connectors | FC/PC – FC/PC |

  - PART II Fiber Optic Patch Cables MIR type II

| Product name | Parameter | Specification |
| --- | --- | --- |
| Fiber Optic Patch Cables MIR type II | Quantity | 4 szt. |
|  | Fiber | InF2 |
|  | Diameter Core | 100 um +/- 5 um |
|  | Numerical aperture | 0.26 +/- 10% in terms of 3.5-5.5 um |
|  | Attenuation | - no more than 0.5 dB/m in terms of 3-4.5 um - no more than 3 dB/m in terms of 4.5-5.5 um |
|  | Length patchord | 1 m +/- 10% |
|  | Diameter outer of the patchcord sheath | 3 mm +/- 10% lub 2 mm +/- 10 % |
|  | Connectors | FC/PC – FC/PC |

  - PART III Fiber Optic Patch Cables MIR type III

| Product name | Parameter | Specification |
| --- | --- | --- |
| Fiber Optic Patch Cables MIR type III | Quantity | 4 szt. |
|  | Fiber | InF2 |
|  | Diameter Core | 200 um +/- 5 um |
|  | Numerical aperture | 0.26 +/- 10% in terms of 3.5-5.5 um |
|  | Attenuation | - no more than 0.5 dB/m in terms of 3-4.5 um - no more than 3 dB/m in terms of 4.5-5.5 um |
|  | Length patchord | 1 m +/- 10% |
|  | Diameter outer of the patchcord sheath | 3 mm +/- 10% lub 2 mm +/- 10 % |
|  | Connectors | FC/PC – FC/PC |